## Slide 1: Virtual Private Network Implementation

## Slide 3: What is a VPN?
  Virtual: Information within a private network is transported over a public network.
  Private: The traffic is encrypted to keep the data confidential.
VPN
VPN
Firewall
CSA
Regional branch with
a VPN enabled
Cisco ISR router
SOHO with a Cisco DSL Router
VPN
Mobile Worker
with a Cisco
VPN Client
Business Partner
with a Cisco Router
Corporate Network
WAN
Internet

## Slide 5: VPN Types – based on technologies
Multiprotocol Label Switching (MPLS) – no encryption by default
SSL
IPSec
SOHO with a Cisco DSL Router
VPN
Internet
IPSec
IPSec

## Slide 6: Types of VPN Networks – based on access methods
MARS
VPN
VPN
Iron Port
Firewall
IPS
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Regional branch with
a VPN enabled
Cisco ISR router
SOHO with a Cisco DSL Router
VPN
Mobile Worker
with a Cisco
VPN Client
Business Partner
with a Cisco Router
Site-to-Site
VPNs
Remote-access
VPNs
Internet
WAN

## Slide 7: Site-to-Site VPN
MARS
VPN
VPN
Iron Port
Firewall
IPS
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Regional branch with
a VPN enabled
Cisco ISR router
SOHO with a Cisco DSL Router
VPN
Business Partner
with a Cisco Router
Site-to-Site
VPNs
Internet
WAN
Hosts send and receive normal TCP/IP traffic through a VPN gateway

## Slide 8: Remote-Access VPNs
MARS
VPN
Iron Port
Firewall
IPS
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Mobile Worker
with a Cisco
VPN Client
Remote-access
VPNs
Internet

## Slide 10: VPN Benefits
Confidentiality
Integrity
Authentication
Antireplay protection

## Slide 11: Core Elements to VPN
Ciphers – Block (DES, 3DES, AES, etc.) and Stream (RC4)
Algorithms – Symmetric (DES, 3DES, AES, etc.) and Asymmetric (RSA, DH)
Hash – MD5, SHA-1, SHA-2
HMAC – Hash + key
Digital Signatures
Key Management

## Slide 12: Key Management
Key Management
Key Generation
Key Storage
Key Verification
Key Exchange
Key Revocation and Destruction

## Slide 13: Keyspace
DES Key | Keyspace | # of Possible Keys
56-bit | 256 11111111 11111111 11111111 11111111 11111111 11111111 11111111 | 72,000,000,000,000,000
57-bit | 257 11111111 11111111 11111111 11111111 11111111 11111111 11111111 1 | 144,000,000,000,000,000
58-bit | 258 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11 | 288,000,000,000,000,000
59-bit | 259 11111111 11111111 11111111 11111111 11111111 11111111 11111111 111 | 576,000,000,000,000,000
60-bit | 260 11111111 11111111 11111111 11111111 11111111 11111111 11111111 1111 | 1,152,000,000,000,000,000
For each bit added to the DES key, the attacker would require twice the amount of time to search the keyspace.
Longer keys are more secure but are also more resource intensive and can affect throughput.
With 60-bit DES
an attacker would
require sixteen
more time than
56-bit DES
Twice as
much time
Four time as
much time

## Slide 15: Types of Keys
224
224
2432
112
Protection up to 20 years
192
192
1776
96
Protection up to 10 years
160
160
1248
80
Protection up to 3 years
Hash
Digital Signature
Asymmetric Key
Symmetric Key
256
256
3248
128
Protection up to 30 years
512
512
15424
256
Protection against quantum computers
Calculations are based on the fact that computing power will continue to grow at its present rate and the ability to perform brute-force attacks will grow at the same rate.
Note the comparatively short symmetric key lengths illustrating that symmetric algorithms are the strongest type of algorithm.

## Slide 16: Key Properties
Shorter keys = faster processing, but less secure
Longer keys = slower processing, but more secure
Notes: More Information: Refer to the National Institute of Standards and Technology (NIST) website at http://www.keylength.com/en/4/ to see updated key length recommendations

## Slide 17: IPSec vs. SSL
IPSec – collection of protocols and algorithms
  ESP and AH: The two primary methods for implementing IPsec. The acronyms stand for Encapsulating Security Payload (ESP), which can do all the features of IPsec, and Authentication Header (AH), which can do many parts of the IPsec objectives, except for the important one of encryption of the data.
  Encryption algorithms for confidentiality: DES, 3DES, AES.
  Hashing algorithms for integrity: MD5, SHA.
  Authentication algorithms: Pre-shared keys (PSK), RSA digital signatures.
  Key management: An example would be Diffie-Hellman (DH), which can be used to dynamically generate symmetrical keys to be used by symmetrical algorithms; PKI, which supports the function of digital certificates issued by trusted CAs; and Internet Key Exchange (IKE), which does a lot of the negotiating and management for us for IPsec to operate.

## Slide 18: IPSec vs. SSL (2)
SSL
  Proven standard
  Widely deployed to secure web services
  Can be labeled as TLS

## Slide 19: IPSec Topology
Works at the network layer, protecting and authenticating IP packets.
  It is a framework of open standards which is algorithm-independent.
  It provides data confidentiality, data integrity, and origin authentication.
Business Partner
with a Cisco Router
Regional Office with a Cisco PIX Firewall
SOHO with a Cisco
SDN/DSL Router
Mobile Worker with a Cisco VPN Client on a Laptop Computer
ASA
Legacy
Concentrator
Main Site
Perimeter
Router
Legacy Cisco
PIX
Firewall
IPsec
POP
Corporate

## Slide 20: IPSec Framework
Diffie-Hellman
DH7

## Slide 21: Confidentiality
DH7
Diffie-Hellman
Key length:
- 56-bits
Key length:
- 56-bits (3 times)
Key length:
- 160-bits
Key lengths:
128-bits
192 bits
256-bits
Least secure Most secure

## Slide 22: Integrity
DH7
Diffie-Hellman
Key length:
- 128-bits
Key length:
- 160-bits)
Least secure Most secure

## Slide 23: Authentication
DH7
Diffie-Hellman

## Slide 24: Pre-shared Key (PSK)
DH7
Diffie-Hellman
[JG1]It?
At the local device, the authentication key and the identity information (device-specific information) are sent through a hash algorithm to form hash_I. One-way authentication is established by sending hash_I to the remote device. If the remote device can independently create the same hash, the local device is authenticated.
The authentication process continues in the opposite direction. The remote device combines its identity information with the preshared-based authentication key and sends it through the hash algorithm to form hash_R. hash_R is sent to the local device. If the local device can independently create the same hash, the remote device is authenticated.

## Slide 25: RSA Signatures
At the local device, the authentication key and identity information (device-specific information) are sent through the hash algorithm forming hash_I. hash_I is encrypted using the local device's private encryption key creating a digital signature. The digital signature and a digital certificate are forwarded to the remote device. The public encryption key for decrypting the signature is included in the digital certificate. The remote device verifies the digital signature by decrypting it using the public encryption key. The result is hash_I.
Next, the remote device independently creates hash_I from stored information. If the calculated hash_I equals the decrypted hash_I, the local device is authenticated. After the remote device authenticates the local device, the authentication process begins in the opposite direction and all steps are repeated from the remote device to the local device.

## Slide 26: Secure Key Exchange
Diffie-Hellman
DH7

## Slide 27: IPSec Framework Protocols
All data is in plaintext.
R1
R2
Data payload is encrypted.
R1
R2
Authentication Header
Encapsulating Security Payload
AH provides the following:
  Authentication
  Integrity
ESP provides the following:
  Encryption
  Authentication
  Integrity

## Slide 28: Authentication Header
Authentication Data
(00ABCDEF)
IP Header + Data + Key
R1
R2
Hash
Recomputed
Hash
(00ABCDEF)
IP Header + Data + Key
Hash
Received
Hash
(00ABCDEF)
=
Data
AH
IP HDR
Data
AH
IP HDR
Internet
1. The IP Header and data payload are hashed
2. The hash builds a new AH
header which is prepended to the original packet
3. The new packet is transmitted to the IPSec peer router
4. The peer router hashes the IP header and data payload, extracts the transmitted hash and compares

## Slide 30: ESP
Diffie-Hellman
DH7

## Slide 31: Function of ESP
ESP
Trailer
ESP
Auth
Provides confidentiality with encryption
Provides integrity with authentication
Router
Router
IP HDR
Data
ESP HDR
New IP HDR
IP HDR
Data
Authenticated
IP HDR
Data
Internet
Encrypted

## Slide 32: Mode Types
IP HDR
ESP HDR
Data
ESP HDR
IP HDR
New IP HDR
Data
Tunnel Mode
Transport Mode
ESP
Trailer
ESP
Auth
ESP
Trailer
ESP
Auth
Authenticated
Authenticated
IP HDR
Data
Encrypted
Encrypted
Original data prior to selection of IPSec protocol mode

## Slide 34: Security Associations
IPSec parameters are configured using IKE

## Slide 35: IKE Phases
Host A
Host B
R1
R2
10.0.1.3
10.0.2.3
IKE Phase 1 Exchange
Negotiate IKE policy sets
DH key exchange
Verify the peer identity
IKE Phase 2 Exchange
Negotiate IPsec policy
Negotiate IPsec policy
Policy 15
DES
MD5
pre-share
DH1
lifetime
Policy 10
DES
MD5
pre-share
DH1
lifetime
Negotiate IKE policy sets
DH key exchange
Verify the peer identity

## Slide 36: IKE Phase 1
Five items to be agreed upon in Phase 1
  Hash algorithm: This could be message digest 5 algorithm (MD5) or Secure Hash Algorithm (SHA) on most devices.
  Encryption algorithm: This could be DES (bad idea, too weak), 3DES (better) or AES (best) with various key lengths. (Longer is better for keys.)
  Diffie-Hellman (DH) group to use: The DH “group” refers to the modulus size (length of the key) to use for the DH key exchange. Group 1 uses 768 bits, group 2 uses 1024, and group 5 uses 1536.
  Authentication methods (PSK or RSA).
  Lifetime

## Slide 38: IKE Phase 1 – First Exchange
Negotiates matching IKE policies to protect IKE exchange
Policy 15
DES
MD5
pre-share
DH1
lifetime
Policy 10
DES
MD5
pre-share
DH1
lifetime
IKE Policy Sets
Policy 20
3DES
SHA
pre-share
DH1
lifetime
Negotiate IKE Proposals
Host A
Host B
R1
R2
10.0.1.3
10.0.2.3

## Slide 39: IKE Phase 1 – Second Exchange
(YB ) mod p = K (YA ) mod p = K
XB
XA
Private value, XA
Public value, YA
Private value, XB
Public value, YB
Alice
Bob
YA
YB
YB = g mod p
XB
YA = g mod p
XA
A DH exchange is performed to establish keying material.
Establish DH Key

## Slide 40: IKE Phase 1 – Third Exchange
Peer authentication methods
  PSKs
  RSA signatures
  RSA encrypted nonces
HR Servers
Remote Office
Corporate Office
Internet
Peer
Authentication
A bidirectional IKE SA is now established.
Authenticate Peer
Phase 1 tunnel is not used to protect user data!!!

## Slide 41: IKE Phase 1 – Aggressive Mode
Host A
Host B
R1
R2
10.0.1.3
10.0.2.3
IKE Phase 1 Aggressive Mode Exchange
Send IKE policy set and R1’s DH key
Calculate shared secret, verify peer identify, and confirm with peer
IKE Phase 2 Exchange
Negotiate IPsec policy
Negotiate IPsec policy
Policy 15
DES
MD5
pre-share
DH1
lifetime
Policy 10
DES
MD5
pre-share
DH1
lifetime
Confirm IKE policy set, calculate shared secret and send R2’s DH key
Authenticate peer and begin Phase 2.

## Slide 42: IKE Phase 2
Negotiate IPsec
Security Parameters
Host A
Host B
R1
R2
10.0.1.3
10.0.2.3
IKE negotiates matching IPsec policies.
Upon completion, unidirectional IPsec Security Associations (SA) are established for each protocol and algorithm combination.

## Slide 43: IPSec VPN Negotiation
IKE Phase 1
IKE Phase 2
IKE SA
IKE SA
IPsec SA
IPsec SA
Host A sends interesting traffic to Host B.
R1 and R2 negotiate an IKE Phase 1 session.
R1 and R2 negotiate an IKE Phase 2 session.
Information is exchanged via IPsec tunnel.
The IPsec tunnel is terminated.
R1
R2
10.0.2.3
IPsec Tunnel
10.0.1.3

## Slide 44: Implementing Site-to-Site VPN (Chapter 7)

## Slide 45
As we consider the VPN options that provide security, we remember that IPsec can perform the following:
  Confidentiality: Using symmetrical encryption algorithms such as 3DES, IDEA, AES, and so on to encrypt clear text into cipher text.
  Data integrity: Using hashing algorithms such as MD5 or SHA and Hashed Message Authentication Code (HMAC) to verify that data has not been manipulated during its transit across the network.
  Authentication: Done by authenticating the VPN peers near the beginning of a VPN session, using PSKs or digital signatures (leveraging digital certificates).
  Hiding the private address space from the Internet: Because IPsec’s Encapsulation Security Protocol (ESP) in tunnel mode encrypts and encapsulates the original packet, and then places a new IP header before forwarding the packet, the Internet sees only the packet as being from the global IP address of one router and destined to the global address of the second router.
IPsec uses two methods for encryption: tunnel and transport mode. If IPsec tunnel mode is used, the IP header and the payload are encrypted. When transport mode is used, only the packet payload is encrypted.

## Slide 46: Protocols required for implementation
See chapter 7 for CISCO CLI configuration in both Router and ASA appliances

## Slide 47: Summary of IPSec Story
In summary , the VPN peers/gateways negotiate the IKE Phase 1 tunnel using aggressive or main mode, and then use Quick mode to establish the IKE Phase 2 tunnel.
They use the IKE Phase 2 tunnel to encrypt and decrypt user packets. Behind the scenes, the IKE Phase 2 tunnel really creates two one-way tunnels: one from R1 to R2 and one from R2 to R1. The end user does not see the process in any detail, and end users do not know the encryption is even being applied to their packets.
So, we could say we have one IKE Phase 1 bidirectional tunnel used for management between the two VPN peers and two IKE Phase 2 unidirectional tunnels used for encrypting and decrypting end-user packets. These tunnels are often referred to as the security agreements between the two VPN peers.
Many times, these agreements are called security associations (SA). Each SA is assigned a unique number for tracking.
See pages 129, 137 – 139 (CLI) for VPN configuration example.

## Slide 48: SSL VPN Concepts
Traditionally, for remote access, IPSec VPN client software is installed on a device.
Someone came up with the brilliant idea that using Secure Sockets Layer (SSL), which is built in to nearly every browser and can communicate securely with the server on the other side, could be used to implement tunnels between the end users and corporate servers or even corporate networks.

## Slide 49: SSL and IPSec Comparison

## Slide 50: SSL and TLS Protocol Framework
TLS and its predecessor SSL are cryptographic protocols that provide secure transactions on the Internet for things such as e-mail, web browsing, instant messaging, and so on. SSL as a protocol was originally developed by Netscape. Most online transactions that are browser based are secured by SSL or TLS.
Both of these protocols provide confidentiality, integrity, and authentication services. These protocols are considered to be operating at the session layer and higher in the OSI logical model.
They both can use the public key infrastructure (PKI) and digital certificates for authentication of the VPN endpoints and for establishing encryption keys that may be used.
Similar to IPsec, these protocols use symmetric algorithms for bulk encryption, and asymmetric algorithms are used for the authentication and for the exchange of keys.

## Slide 52: SSL VPNs
  Integrated security and routing
  Browser-based full network SSL VPN access
SSL VPN
Workplace
Resources
Headquarters
Internet
SSL VPN
Tunnel

## Slide 53: Types of Access

## Slide 54: Full Tunnel Client Access Mode

## Slide 56: Establishing an SSL Session
User using SSL client
User makes a connection to TCP port 443
Router replies with a digitally signed public key
Shared-secret key, encrypted with public key of the server, is sent to the router
Bulk encryption occurs using the shared-secret key with a symmetric encryption algorithm
User software creates a shared-secret key
1
2
3
4
5
SSL VPN enabled ISR router

## Slide 57: SSL VPN Design Considerations
User connectivity
Router feature
Infrastructure planning
Implementation scope